# Sony XDP-4000X Control Protocols

Rev 5 – October 15, 2000

(Includes all known sequences)

Decoded by Matt Dralle / dralle@matronics.com

Bug reports welcome.

Latest document available from:

http://www.matronics.com/XDP-4000X/XDP-4000X-ControlProtocol.doc

Startup Initilization

0  1  2  3  4  5  6  7

SEND:		F0 24 84 8C F7

RECEIVE:	F0 24 8C 31 58 10 F7

SEND:		F0 24 84 8D F7

RECEIVE:	F0 24 8D 20 00 00 10 F7

Digital Equalizer

The following 10-byte sequence is sent in real time each time a parameter change is made to the respective band.  If the L/R Link option is selected, both the Left and Right 10-byte strings are sent in sequence.

Byte 0-4:	Preamble 	(F0 24 B3 F0 02 Hex)

Byte 5:		Band 		(0 to 19) (Odd=Right, Even=Left)

Byte 6:		Frequency 	(0=18 to 184=21.7k) (See end of file for complete breakdown.)

Byte 7:		Level 		(-120(88hex)= -12.0db to 120(78 hex)= +12.0db)

Byte 8:		Q 		(1=0.0 to 255=25.5)

Byte 9:		Terminating 	(F7 Hex)

Actual  EQ data is shown in Italics – in contrast to the Preamble and

Terminating byte shown in Normal.

###### Band 1 / Memory 1 Baseline – All Minimum

Band:	1

Freq:	18Hz

Level:	-12.0

Q:	0.1

0  1  2  3  4  5  6  7  8  9

## F0 24 B3 F0 02 00 00 88 01 F7

Band 1 Baseline / Memory 1 – All Maximum

Band:	1

Freq:	21.7KHz

Level:	+12.0

Q:	25.5

0  1  2  3  4  5  6  7  8  9

F0 24 B3 F0 02 00 B8 78 FF F7

Band:	1			Byte 6 / Range 0 to 184 / Delta 185

Freq:	21.7KHz

##### Level:	-12.0

Q:	0.1

0  1  2  3  4  5  6  7  8  9

### F0 24 B3 F0 02 00 00 88 01 F7 – Min. Baseline

## F0 24 B3 F0 02 00 B8 88 01 F7

Band:	1			Byte 7 / Range –120 to 120 / Delta 240

Freq:	18Hz

#### Level:	+12.0

Q:	0.1

0  1  2  3  4  5  6  7  8  9

##### F0 24 B3 F0 02 00 00 88 01 F7 – Min. Baseline

## F0 24 B3 F0 02 00 00 78 01 F7

F0 24 B3 F0 02 00 0E 88 0E F7 –12 db

F0 24 B3 F0 02 00 0E C4 0E F7 –6 db

F0 24 B3 F0 02 00 0E 00 0E F7 0 db

F0 24 B3 F0 02 00 0E 3C 0E F7 +6 db

F0 24 B3 F0 02 00 0E 78 0E F7 +12 db

Band:	1			Byte 8  / Range 1 to 255 / Delta 254

Freq:	18Hz

#### Level:	-12.0

Q:	25.5

0  1  2  3  4  5  6  7  8  9

F0 24 B3 F0 02 00 00 88 01 F7 – Min. Baseline

F0 24 B3 F0 02 00 00 88 FF F7

###### Band X / Memory 1 Baseline – All Minimum

Band:	2			Byte 5 / Range 0 to 19 / Delta 20 / Odd = Right, Even = Left

Freq:	18Hz

Level:	-12.0

Q:	0.1

## 0  1  2  3  4  5  6  7  8  9

## F0 24 B3 F0 02 00 00 88 01 F7 – Min/Band 01/Mem 1

F0 24 B3 F0 02 02 00 88 01 F7 – Min/Band 02/Mem 1

F0 24 B3 F0 02 12 00 88 01 F7 – Min/Band 10/Mem 1

Band X / Memory 1 Baseline – All Maximum

Band:	2

Freq:	21.7KHz

Level:	+12.0

Q:	25.5

0  1  2  3  4  5  6  7  8  9

F0 24 B3 F0 02 00 B8 78 FF F7 – Max/Band 01/Mem 1

F0 24 B3 F0 02 02 B8 78 FF F7 – Max/Band 02/Mem 1

F0 24 B3 F0 02 12 B8 78 FF F7 – Max/Band 10/Mem 1

Band X / Memory 2 Baseline – All Maximum

Band:	1

Freq:	21.7KHz

Level:	+12.0

Q:	25.5

0  1  2  3  4  5  6  7  8  9

F0 24 B3 F0 02 00 B8 78 FF F7 – Max/Band 01/Mem 1

F0 24 B3 F0 02 00 B8 78 FF F7 – Max/Band 01/Mem 2

Digital Crossover

###### Crossover Adjustment –Level Adjustment – All Settings 0db / Minimum

Left/Right Sub.W (A):		Byte 38/39 / Range –136 (88 hex) to 60 (3c hex) / Delta 196 / -12db to +6db

Left/Right Low (B):		Byte 28/29

Left/Right Mid (C):		Byte 18/19

Left/Right High (D):		Byte 8/9

Actual  Crossover data is shown in Italics – in contrast to the Preamble and

Terminating byte shown in Normal.

0  1  2  3  4  5  6  7  8  9  10 11 12 13 14 15 16 17 18 19

20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39

40 41 42 43 44 45 46 47 48

Left Sub.W:		0db

Right Sub.W:		0db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 00 00 00 00 00 00 00 F7

Left Sub.W:		+. 5db

Right Sub.W:		0db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 05 00

00 00 00 00 00 00 00 00 F7

Left Sub.W:		+1db

Right Sub.W:		0db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 0A 00

00 00 00 00 00 00 00 00 F7

Left Sub.W:		+1db

Right Sub.W:		+. 5db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 0A 05

00 00 00 00 00 00 00 00 F7

Left Sub.W:		+1db

Right Sub.W:		+1db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 0A 0A

00 00 00 00 00 00 00 00 F7

Left Sub.W:		-. 5db

Right Sub.W:		0db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 FB 00

00 00 00 00 00 00 00 00 F7

Left Sub.W:		-1db

Right Sub.W:		0db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 F6 00

00 00 00 00 00 00 00 00 F7

Left Sub.W:		-1db

Right Sub.W:		-. 5db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 F6 FB

00 00 00 00 00 00 00 00 F7

Left Sub.W:		-1db

Right Sub.W:		-1db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 F6 F6

00 00 00 00 00 00 00 00 F7

Left Sub.W:		-12db

Right Sub.W:		-12db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 88 88

00 00 00 00 00 00 00 00 F7

Left Sub.W:		+6db

Right Sub.W:		+6db

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 3C 3C

00 00 00 00 00 00 00 00 F7

Crossover Adjustment – Distance Adjustment – All Settings 0db / Minimum / 0.0m/in

Left/Right Distance (A):	Byte 40-41/42-43 / Range 0 to 2500 / Delta 2500 / 0m to 25.00m (0in to 1000in)

Left/Right Distance (B):	Byte 30-31/32-33

Left/Right Distance (C):	Byte 20-21/22-23

Left/Right Distance (D):	Byte 10-11/12-13

* ASCII Encoded  - Hex 7B ( 123 Decimal) = 1.23m

Actual Crossover data is shown in Italics – in contrast to the Preamble and

Terminating byte shown in Normal.

0  1  2  3  4  5  6  7  8  9  10 11 12 13 14 15 16 17 18 19

20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39

40 41 42 43 44 45 46 47 48

Left Distance (A):	0m

Right Distance (A):	0m

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 00 00 00 00 00 00 00 F7

Left Distance (A):	.01m

Right Distance (A):	0m

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 01 00 00 00 00 00 00 F7

Left Distance (A):	.01m

Right Distance (A):	.01m

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 01 00 01 00 00 00 00 F7

Left Distance (A):	25.0m

Right Distance (A):	.01m

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

09 C4 00 01 00 00 00 00 F7

Left Distance (A):	.01m

Right Distance (A):	25.0m

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 01 09 C4 00 00 00 00 F7

###### Crossover Adjustment – Crossover Points – All Other Settings 0db / Minimum / 0.0m/in

Sub.W Frequency (A) (LPF):		Byte 37

26 hex (38 dec)		= 78 Hz

2C hex (44 dec)	= 99 Hz

Sub.W Attenuation (A) (LPF):		Byte 45

00 hex ( 0 dec) 		= No Cutoff

DC hex (220 dec) 	= -36db

B8 hex (184 dec)	= -72db

Low Frequency (B) (LPF):		Byte 27

56 hex (86 dec)		= 500 Hz

62 hex (98 dec)		= 793 Hz

6e hex (110 dec)	= 1.25kHz

8c hex (140 dec)	= 4.00kHz

92 hex (146 dec)	= 5.03kHz

98 hex (152 dec)	= 6.34kHz

Low Attenuation (B) (LPF):		Byte 35

00 hex ( 0 dec) 		= No Cutoff

E8 hex (232 dec) 	= -24db

B8 hex (184 dec)	= -72db

Low Frequency (B) (HPF):		Byte 26

26 hex (38 dec)		= 78 Hz

2C hex (44 dec)	= 99 Hz

Low Attenuation (B) (HPF):		Byte 34

00 hex ( 0 dec) 		= No Cutoff

DC hex (220 dec) 	= -36db

B8 hex (184 dec)	= -72db

Mid Frequency (C) (LPF):		Byte 17

8c hex (140 dec)	= 4.00kHz

92 hex (146 dec)	= 5.03kHz

98 hex (152 dec)	= 6.34kHz

Mid Attenuation (C) (LPF):		Byte 25

00 hex ( 0 dec) 		= No Cutoff

E8 hex (232 dec) 	= -24db

B8 hex (184 dec)	= -72db

Mid Frequency (C) (HPF):		Byte 16

26 hex (38 dec)		= 78 Hz

2C hex (44 dec)	= 99 Hz

56 hex (86 dec)		= 500 Hz

62 hex (98 dec)		= 793 Hz

6e hex (110 dec)	= 1.25kHz

Mid Attenuation (C) (HPF):		Byte 24

00 hex ( 0 dec) 		= No Cutoff

DC hex (220 dec) 	= -36db

B8 hex (184 dec)	= -72db

High Frequency (D) (HPF):		Byte 6

8c hex (140 dec)	= 4.00kHz

92 hex (146 dec)	= 5.03kHz

98 hex (152 dec)	= 6.34kHz

High Attenuation (D) (HPF):		Byte 14

00 hex ( 0 dec) 		= No Cutoff

E8 hex (232 dec) 	= -24db

B8 hex (184 dec)	= -72db

Actual  Crossover data is shown in Italics – in contrast to the Preamble and Terminating byte shown in Normal.  Only a subset of the possible combinations are shown below.  Review byte breakdown above for complete information.

0  1  2  3  4  5  6  7  8  9  10 11 12 13 14 15 16 17 18 19

20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39

40 41 42 43 44 45 46 47 48

Low (B) Attenuation (HPF):		-72db/oct

Low (B) Frequency (HPF):		78Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 B8 00 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (HPF):		-72db/oct

Low (B) Frequency (HPF):		98Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 2C 56 00 00 00 00 00 00 B8 00 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (HPF):		0db/oct

Low (B) Frequency (HPF):		--Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (HPF):		-36db/oct

Low (B) Frequency (HPF):		78Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 DC 00 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (HPF):		-72db/oct

Low (B) Frequency (HPF):		78Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 B8 00 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-24db/oct

Low (B) Frequency (LPF):		500Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 E8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-72db/oct

Low (B) Frequency (LPF):		500Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 B8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-72db/oct

Low (B) Frequency (LPF):		793Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 62 00 00 00 00 00 00 00 B8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-72db/oct

Low (B) Frequency (LPF):		1.25kHz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 6E 00 00 00 00 00 00 00 B8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-72db/oct

Low (B) Frequency (LPF):		4.00kHz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 8C 00 00 00 00 00 00 00 B8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-72db/oct

Low (B) Frequency (LPF):		5.03kHz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 92 00 00 00 00 00 00 00 B8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Low (B) Attenuation (LPF):		-72db/oct

Low (B) Frequency (LPF):		6.34kHz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 98 00 00 00 00 00 00 00 B8 FF 2C 00 00

00 00 00 00 00 00 00 00 F7

Sub.W (A) Attenuation:		0db/oct

Sub.W (A) Frequency:			--Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 00 00 00 00 00 00 00 F7

Sub.W (A) Attenuation:		-36db/oct

Sub.W (A) Frequency:			78Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 00 00 00 00 DC 00 00 F7

Sub.W (A) Attenuation:		-72db/oct

Sub.W (A) Frequency:			78Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 26 00 00

00 00 00 00 00 B8 00 00 F7

Sub.W (A) Attenuation:		-36db/oct

Sub.W (A) Frequency:			99Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 2C 00 00

00 00 00 00 00 DC 00 00 F7

Sub.W (A) Attenuation:		-72db/oct

Sub.W (A) Frequency:			99Hz

F0 24 B3 F0 04 FE 98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00 00 00 FF 2C 00 00

00 00 00 00 00 B8 00 00 F7

Write All Equalizer Data to DSP NVRAM

Following the preamble, 10 sets of 20, 3-byte data sets are sent representing the Frequency, Level, and Q of Bands 1 through 20, for Memorys 1-10 respectively.  A terminating “F7” is appended to the end of the sequence.  Executing this full sequence writes all EQ data to the DSP’s NVRAM.

Preamble:				F0 24 B3 F0 02 FF

Memory 1, 	Band 1:		0E 00 0E

Band 2:		0E 00 0E

Band 3:		20 00 0E

Band 4:		20 00 0E

Band 5:		32 00 0E

Band 6:		32 00 0E

Band 7:		44 00 0E

Band 8:		44 00 0E

Band 9:		56 00 0E

Band 10:		56 00 0E

Band 11:		68 00 0E

Band 12:		68 00 0E

Band 13:		7A 00 0E

Band 14:		7A 00 0E

Band 15:		8C 00 0E

Band 16:		8C 00 0E

Band 17:		9E 00 0E

Band 18:		9E 00 0E

Band 19:		B0 00 0E

Band 20:		B0 00 0E

Memory 2,	Band 1/2:		0E 00 0E 0E 00 0E

Band 3/4:		20 00 0E 20 00 0E

Band 5/6:		32 00 0E 32 00 0E

Band 7/8:		44 00 0E 44 00 0E

Band 9/10:		56 00 0E 56 00 0E

Band 11/12:	68 00 0E 68 00 0E

Band 13/14:	7A 00 0E 7A 00 0E

Band 15/16:	8C 00 0E 8C 00 0E

Band 17/18:	9E 00 0E 9E 00 0E

Band 19/20:	B0 00 0E B0 00 0E

Memory 3,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 4,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 5,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 6,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 7,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 8,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 9,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 10,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

End of Data:			F7

Write All Crossover Data to DSP NVRAM

Following the preamble, ten 42-byte location specific data packets are transmitted followed by a terminating “F7”.  These are the same 42 byte data packets that are sent during real time adjustment as described above less the Real time Preamble.  The other difference is that executing this full sequence writes all of the data to the DSP’s NVRAM, whereas the real time changes do not.

Preamble:			F0 24 B3 F0 04 FF

Location #1 Data:	98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00

00 E8 FF 2C 00 00 00 00 00 00 00 DC 00 00

Location #2 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #3 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #4 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #5 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #6 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #7 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #8 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #9 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #10 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

End of Data:		F7

Write Equalizer Memory Location Text Labels

87 Byte sequence that writes text to all 10 Text Description NVRAM locations for Equalizer settings.  Must transmit all 10 locations at once.

0  1  2  3  4  5  6  7  8

Preamble:				F0 24 B3 F2 02 FF

ASCII “MEMORY 1”:		4D 45 4D 4F 52 59 20 31 00

ASCII “MEMORY 2”:		4D 45 4D 4F 52 59 20 32 00

ASCII “MEMORY 3”:		4D 45 4D 4F 52 59 20 33 00

ASCII “MEMORY 4”:		4D 45 4D 4F 52 59 20 34 00

ASCII “MEMORY 5”:		4D 45 4D 4F 52 59 20 35 00

ASCII “MEMORY 6”:		4D 45 4D 4F 52 59 20 36 00

ASCII “MEMORY 7”:		4D 45 4D 4F 52 59 20 37 00

ASCII “MEMORY 8”:		4D 45 4D 4F 52 59 20 38 00

ASCII “MEMORY 9”:		4D 45 4D 4F 52 59 20 39 00

ASCII “MEMORY10”:		4D 45 4D 4F 52 59 31 30 00

End of Text:			F7

Write Crossover Memory Location Text Labels

87 Byte sequence that writes text to all 10 Text Description NVRAM locations for Crossover settings.  Must transmit all 10 locations at once.

0  1  2  3  4  5  6  7  8

Preamble:				F0 24 B3 F2 04 FF

ASCII “MEMORY 1”:		4D 45 4D 4F 52 59 20 31 00

ASCII “MEMORY 2”:		4D 45 4D 4F 52 59 20 32 00

ASCII “MEMORY 3”:		4D 45 4D 4F 52 59 20 33 00

ASCII “MEMORY 4”:		4D 45 4D 4F 52 59 20 34 00

ASCII “MEMORY 5”:		4D 45 4D 4F 52 59 20 35 00

ASCII “MEMORY 6”:		4D 45 4D 4F 52 59 20 36 00

ASCII “MEMORY 7”:		4D 45 4D 4F 52 59 20 37 00

ASCII “MEMORY 8”:		4D 45 4D 4F 52 59 20 38 00

ASCII “MEMORY 9”:		4D 45 4D 4F 52 59 20 39 00

ASCII “MEMORY10”:		4D 45 4D 4F 52 59 31 30 00

End of Text:			F7

Read All Equalizer Data from DSP NVRAM

The 7-byte “Request Sequence” is first sent to the DSP.  The DSP will respond with the following 4-byte preamble and then 10 sets of 20, 3-byte data sets representing the Frequency, Level, and Q of Bands 1 through 20, for Memories 1-10 respectively.  A terminating “F7” is appended to the end of the sequence.

SEND:

0  1  2  3  4  5  6  7  8

Request Sequence:		F0 24 84 DC 02 FF F7

RECEIVE:

Preamble:				F0 24 DC FF

Memory 1, 	Band 1:		0E 00 0E

Band 2:		0E 00 0E

Band 3:		20 00 0E

Band 4:		20 00 0E

Band 5:		32 00 0E

Band 6:		32 00 0E

Band 7:		44 00 0E

Band 8:		44 00 0E

Band 9:		56 00 0E

Band 10:		56 00 0E

Band 11:		68 00 0E

Band 12:		68 00 0E

Band 13:		7A 00 0E

Band 14:		7A 00 0E

Band 15:		8C 00 0E

Band 16:		8C 00 0E

Band 17:		9E 00 0E

Band 18:		9E 00 0E

Band 19:		B0 00 0E

Band 20:		B0 00 0E

Memory 2,	Band 1/2:		0E 00 0E 0E 00 0E

Band 3/4:		20 00 0E 20 00 0E

Band 5/6:		32 00 0E 32 00 0E

Band 7/8:		44 00 0E 44 00 0E

Band 9/10:		56 00 0E 56 00 0E

Band 11/12:	68 00 0E 68 00 0E

Band 13/14:	7A 00 0E 7A 00 0E

Band 15/16:	8C 00 0E 8C 00 0E

Band 17/18:	9E 00 0E 9E 00 0E

Band 19/20:	B0 00 0E B0 00 0E

Memory 3,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 4,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 5,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 6,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 7,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 8,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 9,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

Memory 10,	Band 1-20:		0E 00 0E 0E 00 0E 20 00 0E 20 00 0E 32 00 0E 32 00 0E

44 00 0E 44 00 0E 56 00 0E 56 00 0E 68 00 0E 68 00 0E 7A 00 0E 7A 00 0E 8C 00 0E 8C 00 0E 9E 00 0E 9E 00 0E

B0 00 0E B0 00 0E

End of Text:			F7

Read Equalizer Memory Location Text Labels

SEND:

0  1  2  3  4  5  6  7  8

Request Sequence:		F0 24 84 CA 02 FF F7

RECEIVE:

Preamble:				F0 24 CA 02 FF

ASCII “MEMORY 1”:		4D 45 4D 4F 52 59 20 31 00

ASCII “MEMORY 2”:		4D 45 4D 4F 52 59 20 32 00

ASCII “MEMORY 3”:		4D 45 4D 4F 52 59 20 33 00

ASCII “MEMORY 4”:		4D 45 4D 4F 52 59 20 34 00

ASCII “MEMORY 5”:		4D 45 4D 4F 52 59 20 35 00

ASCII “MEMORY 6”:		4D 45 4D 4F 52 59 20 36 00

ASCII “MEMORY 7”:		4D 45 4D 4F 52 59 20 37 00

ASCII “MEMORY 8”:		4D 45 4D 4F 52 59 20 38 00

ASCII “MEMORY 9”:		4D 45 4D 4F 52 59 20 39 00

ASCII “MEMORY10”:		4D 45 4D 4F 52 59 31 30 00

End of Text:			F7

Read All Crossover Data from DSP NVRAM

The 7-byte “Request Sequence” is first sent to the DSP.  The DSP will respond with the following 4-byte preamble, then ten 42-byte location specific data packets are transmitted followed by a terminating “F7”.  These are the same 42 byte data packets that are sent during real time adjustment as described above less the Real time Preamble.

SEND:

0  1  2  3  4  5  6  7  8

Request Sequence:	F0 24 84 D4 04 FF F7

RECEIVE:

Preamble:			F0 24 D4 FF

Location #1 Data:	98 FF 00 00 00 00 00 00 E8 00 62 92 00 00

00 00 00 00 00 00 26 56 00 00 00 00 00 00

00 E8 FF 2C 00 00 00 00 00 00 00 DC 00 00

Location #2 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #3 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #4 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #5 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #6 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #7 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #8 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #9 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

Location #10 Data:	92 FF 00 00 00 00 00 00 B8 00 62 92 00 00

00 00 00 00 B8 B8 26 62 00 00 00 00 00 00

B8 B8 FF 26 00 00 00 00 00 00 00 B8 00 00

End of Data:		F7

Read Crossover Memory Location Text Labels

SEND:

0  1  2  3  4  5  6  7  8

Request Sequence:		F0 24 84 CA 04 FF F7

RECEIVE:

Preamble:				F0 24 CA 04 FF

ASCII “MEMORY 1”:		4D 45 4D 4F 52 59 20 31 00

ASCII “MEMORY 2”:		4D 45 4D 4F 52 59 20 32 00

ASCII “MEMORY 3”:		4D 45 4D 4F 52 59 20 33 00

ASCII “MEMORY 4”:		4D 45 4D 4F 52 59 20 34 00

ASCII “MEMORY 5”:		4D 45 4D 4F 52 59 20 35 00

ASCII “MEMORY 6”:		4D 45 4D 4F 52 59 20 36 00

ASCII “MEMORY 7”:		4D 45 4D 4F 52 59 20 37 00

ASCII “MEMORY 8”:		4D 45 4D 4F 52 59 20 38 00

ASCII “MEMORY 9”:		4D 45 4D 4F 52 59 20 39 00

ASCII “MEMORY10”:		4D 45 4D 4F 52 59 31 30 00

End of Text:			F7

Integer to Frequency Map For EQ Center Configuration

Frequency Breakdown (Note that some Frequencies repeat for a

given Integer value in the low frequencies):

Integer	Frequency

- 18

- 18

- 19

- 20

- 21

- 22

- 22

- 23

- 24

- 25

- 26

- 27

- 28

- 30

- 31

- 32

- 33

- 35

- 36

- 37

- 39

- 40

- 42

- 44

- 45

- 47

- 49

- 51

- 53

- 55

- 57

- 60

- 62

- 64

- 67

- 70

- 72

- 75

- 78

- 81

- 85

- 88

- 91

- 95

- 99

- 103

- 107

- 111

- 115

- 120

- 125

- 129

- 135

- 140

- 145

- 151

- 157

- 163

- 170

- 176

- 183

- 190

- 198

- 206

- 214

- 222

- 231

- 240

- 250

- 259

- 270

- 280

- 291

- 303

- 314

- 327

- 340

- 353

- 367

- 381

- 396

- 412

- 428

- 445

- 462

- 481

- 500

- 519

- 540

- 561

- 583

- 606

- 629

- 654

- 680

- 707

- 734

- 763

- 793

- 824

- 857

- 890

- 925

- 962

- 1.00

- 1.03

- 1.08

- 1.12

- 1.16

- 1.21

- 1.25

- 1.30

- 1.36

- 1.41

- 1.46

- 1.52

- 1.58

- 1.64

- 1.71

- 1.78

- 1.85

- 1.92

- 2.00

- 2.07

- 2.16

- 2.24

- 2.33

- 2.42

- 2.51

- 2.61

- 2.72

- 2.82

- 2.93

- 3.05

- 3.17

- 3.29

- 3.42

- 3.56

- 3.70

- 3.84

- 4.00

- 4.15

- 4.32

- 4.48

- 4.66

- 4.84

- 5.03

- 5.23

- 5.44

- 5.65

- 5.87

- 6.10

- 6.34

- 6.59

- 6.85

- 7.12

- 7.40

- 7.69

- 8.00

- 8.31

- 8.64

- 8.97

- 9.33

- 9.69

- 10.0

- 10.4

- 10.8

- 11.3

- 11.7

- 12.2

- 12.6

- 13.1

- 13.7

- 14.2

- 14.8

- 15.3

- 16.0

- 16.6

- 17.2

- 17.9

- 18.6

- 19.3

- 20.0

- 20.9

- 21.7